## Slide 1: Encryption in the microarchitectural world
Ping-Lun Wang, Fraser Brown, Riccardo Paccagnella,
Eyal Ronen, Riad S. Wahby, and Yuval Yarom
RWC, 03/09/2026

## Slide 2: Arch vs. μArch components
µArch
ISA
Cache hierarchy
Branch predictor (BP)
…
▲ CPU
Credit: irasutoya.com
Instruction set
Architectural registers
…
Architectural (Arch) components
Microarchitectural (μArch) components

## Slide 3: μWMs: hidden computers in the CPU
▲ CPU
µArch weird machines (µWMs)
µArch
ISA
🤯 Prevents code analysis
😎 Hides computational states
😈 Defeats debuggers and emulators
µWMs: difficult to analyze!
Credit: irasutoya.com
🤔 Seems to be great for program obfuscation?

## Slide 4: Existing µWMs need improvements…
Size (thousands of logic gates)
Accuracy (%)
💥 Not scalable for large computations
_32BitValueToCacheState(C_arch, C1, NULL);
_32BitValueToCacheState(D_arch, D1, NULL);
_32BitValueToCacheState(E_arch, E, NULL);
_32BitValueToCacheState(K[0], K0, NULL);
_32BitValueToCacheState(W_arch, W, NULL);
LeftShift(A1, A1, 27);
mfence();
lfence();
trash = _32BitAnd(B1, C1, B_AND_C, trash);
mfence();
lfence();
trash = _32BitNot(B2, NOT_B, trash);
mfence();
lfence();
trash = _32BitAnd(NOT_B, D1, NOT_B_AND_D, trash); … // 128 lines in total
💥 Difficult to create new µWMs

## Slide 5: Our work: Flexo and Transient Arch Execution
Credit: irasutoya.com
ISA
ISA
✨ Improved construction!
✨ Compiler for μWMs!
✨ μWM binary packer!
✨ New μWM: weird programs!
✨ Large state storage!
✨ 543× speedup!
Flexo
Transient Arch Execution
Bending microarchitectural weird machines towards practicality [USENIX Security 24]
Transient architectural execution:
from weird gates to weird programs [SP 26]

## Slide 6: Background
μWMs and weird computation

## Slide 7: From Arch to μArch “weird” computation
Microarchitectural “Weird” Computation
Architectural Computation
✅
State: registers and memory
Architecturally visible
✅
Compute: ISA instructions
ADD, AND, MOV, JMP
🔥
State: “weird” registers using μArch state
Cached = 1
Not cached = 0
🔥
Compute: hardware side-effects
“Weird gates” compute with memory operations during transient execution
Credit: irasutoya.com

## Slide 8: The construction of a weird gate
Transient execution
Exec
How weird gates work
1️⃣
Trigger transient execution
2️⃣
Compute with input latency
3️⃣
Access output weird registers
Time
1️⃣
2️⃣
Init
Inputs
in μArch
End
Outputs in μArch
3️⃣

## Slide 9: The construction of a weird gate
if (condition()) {
tmp += out[in1[0] + in2[0]];
}
end();
How weird gates work
1️⃣
Trigger transient execution
Branch misprediction, return address misprediction, etc.
2️⃣
Compute with input latency
Depending on the cache state, input weird registers may have different latency.
Cached → short cache hit
Not cached → long cache miss
3️⃣
Access output weird registers
Write the results to output weird registers via memory loads.
condition()
returns
BP predicts
(incorrectly)
Time
Run tmp += …
Cleanup tmp += …
Run end()
Run if(…)
Transient execution
Misprediction
Slow…

## Slide 10: The construction of a weird gate
if (condition())
tmp += out[in1[0] + in2[0]];
How weird gates work
1️⃣
Trigger transient execution
Branch misprediction, return address misprediction, etc.
2️⃣
Compute with input latency
Depending on the cache state, input weird registers may have different latency.
Cached → short cache hit
Not cached → long cache miss
3️⃣
Access output weird registers
Write the results to output weird registers via memory loads.
Input weird registers
Cached
Not cached
Value
available
Value
available
Time

## Slide 11: The construction of a weird gate
if (condition())
tmp += out[in1[0] + in2[0]];
How weird gates work
1️⃣
Trigger transient execution
Branch misprediction, return address misprediction, etc.
2️⃣
Compute with input latency
Depending on the cache state, input weird registers may have different latency.
Cached → short cache hit
Not cached → long cache miss
3️⃣
Access output weird registers
Write the results to output weird registers via memory loads.
Output weird register
Initial state: not cached
After execution
  Result is 0: not cached
  Result is 1: cached

## Slide 12: Prior work’s AND gate
Time
condition() returns
Transient execution
if (condition())
tmp += out[in1[0] + in2[0]];
Misprediction
Input
out = 1
(1, 1)
out = 0
(1, 0)
(0, 1)
out = 0
(0, 0)
out = 0
How the AND gate works
1️⃣
Trigger transient execution
CPU mispredicts the branch and executes the gate transiently.
2️⃣
Compute with input latency
Both in1 and in2 are fetched at the same time (no dependency!)
Addition (in1[0] + in2[0]) is computed after the loads
3️⃣
Access output weird registers
out is fetched only when 2️⃣ finished before transient execution ends.

## Slide 13: Prior work’s other types of gates
if (condition()) {
tmp += out[in1[0]];
tmp += out[in2[0] + in3[0]];
}
▲ AND & OR gate
if (condition()) {
tmp += out[in1[0]];
tmp += out[in2[0]];
}
if (in[0])
tmp += out[delay()];
▲ OR gate
▲ NOT gate
OR
AND

## Slide 14: Compose weird gates into weird circuits
in1
in2
out
▲ Prior work’s XOR circuit (5 weird gates)
✨ Flexo can do this in one gate!!

## Slide 15: Flexo
Making weird gates much faster and much more accurate

## Slide 16: Flexo’s construction: differential encoding
Flexo
 |  | Value
0 | 1 | Binary 0
1 | 0 | Binary 1
 |  | Value
0 | 1 | Binary 0
1 | 0 | Binary 1
0/1
WR
0/1
WR+
0 | 0 | Invalid!
1 | 1 | Invalid!
WR–
0/1

## Slide 17: Differential encoding → many benefits!
Flexo
+-
+-
+-
✨ Powerful gates!
✨ Higher accuracy!

## Slide 18: Applying Flexo’s differential encoding
out is 1 when in1 is 1 AND in2 is 0
out = in1 ∧ ¬in2
out+ = in1+ ∧ in2–
Flexo
in1 | in2 | out
1 | 0 | 1
0 | 1 | 1
1 | 1 | 0
0 | 0 | 0

## Slide 19: Applying Flexo’s differential encoding
in1 | in2 | out
1 | 0 | 1
0 | 1 | 1
1 | 1 | 0
0 | 0 | 0
out+ = in1+ ∧ in2–
out+ = in1– ∧ in2+
out– = in1+ ∧ in2+
out– = in1– ∧ in2–
out+ = (in1+ ∧ in2–) ∨ (in1– ∧ in2+)
out– = (in1+ ∧ in2+) ∨ (in1– ∧ in2–)
OR them together
✨ Only AND & OR operations!!

## Slide 20: New encoding → much more scalable gates!
if (condition()) {
tmp += out_p[in1_p[0] + in2_m[0]];
tmp += out_p[in1_m[0] + in2_p[0]];
tmp += out_m[in1_p[0] + in2_p[0]];
tmp += out_m[in1_m[0] + in2_m[0]];
}
AND operators
OR operators
in1 | in2 | out
1 | 0 | 1
0 | 1 | 1
1 | 1 | 0
0 | 0 | 0
✨ Any gate with ≤ 4 inputs works!!
E.g., 4-bit XOR or 2-bit adder

## Slide 21: Error correction with dynamic voting
Prior work (GoT[1]): 3-out-of-5 voting
+-
+-
+-
Run 1: Invalid!
Run 2: Invalid!
Run 3: 1
→ Output 1
Flexo: rerun only when error occurs
[1] The Gates of Time: Improving Cache Attacks with Transient Execution, Katzman et al., USENIX Security ‘23
✨ Higher accuracy & less overhead!!
Run 1: 1
Run 2: 1
Run 3: 1
Run 4: 1
Run 5: 0
→ Output 1

## Slide 22: Flexo’s compiler: the first compiler for μWMs
void __weird__sha1_round(
unsigned* input,
unsigned* output, unsigned* error_output
) {
unsigned a = input[0];
unsigned b = input[1];
unsigned c = input[2];
unsigned d = input[3];
unsigned e = input[4];
unsigned w = input[5];
unsigned k = 0x5A827999;
unsigned f = (b & c) | ((~b) & d);
unsigned temp = ROL(a, 5) + f + e + w + k;
output[0] = temp;
output[1] = a;
output[2] = ROL(b, 30);
output[3] = c;
output[4] = d;
}
_32BitValueToCacheState(C_arch, C1, NULL);
_32BitValueToCacheState(D_arch, D1, NULL);
_32BitValueToCacheState(E_arch, E, NULL);
_32BitValueToCacheState(K[0], K0, NULL);
_32BitValueToCacheState(W_arch, W, NULL);
LeftShift(A1, A1, 27);
mfence();
lfence();
trash = _32BitAnd(B1, C1, B_AND_C, trash);
mfence();
lfence();
trash = _32BitNot(B2, NOT_B, trash);
mfence();
lfence();
trash = _32BitAnd(NOT_B, D1, NOT_B_AND_D, trash);
mfence();
lfence();
trash = _32BitOr(B_AND_C, NOT_B_AND_D, B_AND_C_OR_NOT_B_AND_D, trash);
mfence();
lfence();
trash = _32BitAdder_impl(A1, B_AND_C_OR_NOT_B_AND_D, SUM_1, WORDSIZE, trash);
mfence();
lfence();
…
(128 lines in total)
(21 lines in total)
😇 No low-level details
✨ Optimizations!

## Slide 23: UPX + Flexo: the first μWM binary packer
Pack
Unpack
Decompress
Compress
UPX + WM
Input program
Packed program
</>
Decrypt
(Using Flexo)
Encrypt
chksum
chksum
Roughly 1 minute to unpack 132 KB using Simon
(5 minutes using AES)
Slower, but defeats anti-virus tools!

## Slide 24: Limitations of weird gates
Branches and memory operations are not scalable
A weird register can only store 1 bit
A weird gate can only compute 4 bits at a time
🤔 Can we make μWMs more powerful?

## Slide 25: Transient Arch Exec
From weird gates to weird programs

## Slide 26: Transient arch exec: μArch state + Arch compute
Architectural Computation
✅
State: registers and memory
Architecturally visible
✅
Compute: ISA instructions
ADD, AND, MOV, JMP
Microarchitectural “Weird” Computation
🔥
State: “weird” registers using μArch state
Cached = 1
Not cached = 0
🔥
Compute: hardware side-effects
“Weird gates” compute with transient memory operations
Credit: irasutoya.com
1️⃣ μArch to Arch
2️⃣ Arch compute
3️⃣ Arch to μArch
Plan: run 1️⃣2️⃣3️⃣ in one transient execution window

## Slide 27: Convert cache states to Arch states
int cache2arch(int *input) {
if (input[0]) return 0;
else return 1;
}
input[0] is set to 0 architecturally
Return value (during transient execution):
  input is cached: return 1
  input is not cached: return 0

## Slide 28: Convert cache states to Arch states
int cache2arch(int *input) {
if (input[0]) return 0;
else return 1;
}
int cache2arch(int *input) {
if (input[0]) return 0;
else return 1;
}
Cached
Not cached
0
???
Misprediction

## Slide 29: Weird functions: new computational abilities
if (condition()) {
int tmp_in1 = cache2arch(in1);
int tmp_in2 = cache2arch(in2);
if (tmp_in1 ^ tmp_in2) load(out);
}
✨ Powerful instructions (e.g., AES-NI)!
✨ Branch instructions!
✨ Dynamically access weird registers!
✨ Access to the (read-only) main memory!
✨ Can be composed into weird programs!
Details in our paper!

## Slide 30: Takeaways
✨ Flexo: fast and accurate weird gates with compiler support
Bending microarchitectural weird machines towards practicality
Transient architectural execution: from weird gates to weird programs
Contact: Ping-Lun Wang, pinglunw@andrew.cmu.edu
✨ Transient Arch Exec: weird programs with powerful computational abilities
✨ μWMs are practical for program obfuscation or other attacks
▲ Flexo
▲ TAE